## Slide 1: ICMP & IGMP -by Hitesh Nautiyal

## Slide 2: ICMP :-
A network device uses the Internet Control Message Protocol (ICMP) to diagnose network communication problems. Information about whether data is reaching its desired destination on time is primarily determined by ICMP. Commonly, the ICMP protocol is used on network devices, such as routers. ICMP is essential for error reporting and testing and it can also be used in distributed denial-of-service attacks.

## Slide 3: How ICMP Work ?
In ICMP, no connection is formed. The message is simply sent. In addition, unlike TCP and UDP, which specify the ports to which information is sent, ICMP does not specify a specific port to which information will be received.
When the network disables the delivery of packets to the destination device, it generates and sends error messages to the sender device. Error messages include time exceeded, parameter problem, destination unreachable, network congestion, etc.
An IP(Internet Protocol) datagram is sent from one device to another through multiple routers and intermediaries when it is sent from one device to. There can be an error in forwarding that IPV4 datagram. Hence, ICMP messages are divided into two broad categories :
Error messages
Query messages

## Slide 4: ICMP Message Format :-

## Slide 5: Types of ICMP Error Reporting Messages :-
Message "Unable to reach destination": Hosts and routers send this message when IP packets cannot be routed to their destination. An intermediary router can discard a datagram and send an unreachable message to sender A if recipient B does not receive it.
Source quench message: When the network is congested or when the source is sending packets faster than the router can handle, the host or router will send this message.
Timeout message: The host/router sends this message if the datagram lifetime value is reduced to zero or if the destination address does not receive all packets at the specified time interval. For example, after a packet is sent from the 1000-unit layer to the 200-unit layer, the packet is split into five fragments. If all fragments do not reach the destination within the specified time, all fragments are discarded and a timeout message is sent to the source.
Parameter problem message: The host/router sends this message if the datagram parameters are not set correctly. Used to indicate an error in the datagram header field.
Redirect message: The host/router sends this message to update the host's routing table. For example, sender A wants to send a message to recipient B, and there is a router between them. A then sends the data to the router, which sends the message to B and the redirect message to A, allowing A to update the routing table.

## Slide 6: IGMP :-
It stands for Internet group message protocol. IGMP is a multicasting communication protocol that uses resources efficiently to broadcast message/data packets. Hosts and nearby routers use it for multicasting communication with IP networks. IGMP can be utilized in streaming media, games, or web conferencing tools since multicast communication can have multiple senders and receivers.

## Slide 7: IGMP Message Format :-