## Slide 1: CHANNELIZATION & DATA LINK LAYER -by Hitesh Nautiyal

## Slide 2: Channelization & their protocols:-
Channelization is basically a method that provides the multiple-access and in this, the available bandwidth of the link is shared in time, frequency, or through the code in between the different stations.
Channelization Protocols are broadly classified as follows:
FDMA(Frequency-Division Multiple Access)
TDMA(Time-Division Multiple Access)
CDMA(Code-Division Multiple Access)

## Slide 3: FDMA:-
With the help of this technique, the available bandwidth is divided into frequency bands. Each station is allocated a band in order to send its data. Or in other words, we can say that each band is reserved for a specific station and it belongs to the station all the time.
Each station makes use of the bandpass filter in order to confine the frequencies of the transmitter.
In order to prevent station interferences, the allocated bands are separated from one another with the help of small guard bands.
The Frequency-division multiple access mainly specifies a predetermined frequency for the entire period of communication.
Stream of data can be easily used with the help of FDMA.

## Slide 4: TDMA:-
Time-Division Multiple access is another method to access the channel for shared medium networks.
With the help of this technique, the stations share the bandwidth of the channel in time.
A time slot is allocated to each station during which it can send the data.
Data is transmitted by each station in the assigned time slot.
There is a problem in using TDMA and it is due to TDMA the synchronization cannot be achieved between the different stations.
When using the TDMA technique then each station needs to know the beginning of its slot and the location of its slot.
If the stations are spread over a large area, then there occur propagation delays; in order to compensate this guard, times are used.
The data link layer in each station mainly tells its physical layer to use the allocated time slot.

## Slide 5: CDMA:-
CDMA(code-division multiple access) is another technique used for channelization.
CDMA technique differs from the FDMA because only one channel occupies the entire bandwidth of the link.
The CDMA technique differs from the TDMA because all the stations can send data simultaneously as there is no timesharing.
The CDMA technique simply means communication with different codes.
In the CDMA technique, there is only one channel that carries all the transmission simultaneously.
CDMA is mainly based upon the coding theory; where each station is assigned a code, Code is a sequence of numbers called chips.
The data from the different stations can be transmitted simultaneously but using different code languages.

## Slide 6: Functions of Data Link Layer:-
For effective data communication between two directly connected transmitting and receiving stations the data link layer has to carry out a number of specific functions as follows:
1. Services provided to the network layer:
A well-defined service interface to the network layer on source machine to the network layer on destination machine.
2. Frame synchronization:
The source machine sends data in blocks called frames to the destination machine. The starting and ending of each frame should be recognised by the destination machine.
3. Flow control
The source machine must not send data frames at a rate faster than the destination machine can accept them.
4. Error control:
The errors made in bits during transmission from source to destination machines must be detected and corrected.
5. Addressing:
On a multipoint line, such as many machines connected together (LAN), the identity of the individual machines must be specified while transmitting the data frames.
6. Control and data on same link:
The data and control information is combined in a frame and transmitted from the source to destination machine. The destination machine must be able to recognise control information from the data being transmitted.
7. Link Management:
The initiation, maintenance and termination of the link between the source and destination are required for effective exchange of data. It requires co-ordination and co-operation among stations. Protocols or procedures are required for the link management.

## Slide 7: CheckSum:-
Checksum is an error detection method
Case-01: Result = 0
If the result is zero,
Receiver assumes that no error occurred in the data during the transmission.
Receiver accepts the data.
Case-02: Result ≠ 0
If the result is non-zero,
Receiver assumes that error occurred in the data during the transmission.
Receiver discards the data and asks the sender for retransmission.

## Slide 8: Example :-
Problem-
Checksum value of 1001001110010011 and 1001100001001101 of 16 bit segment is -
(a) 1010101000011111
(b) 1011111000100101
(c) 1101010000011110
(d) 1101010000111111
Solution-
We apply the above discussed algorithm to calculate the checksum.
1001001110010011 + 1001100001001101 = 10010101111100000
Since, the result consists of 17 bits, so 1 bit is wrapped around and added to the result.
0010101111100000 + 1 = 0010101111100001
Now, result consists of 16 bits.
Now, 1’s complement is taken which is 1101010000011110.
Thus, checksum value = 1101010000011110.
Thus, Option (C) is correct.